## Slide 1: MADWEC 3.0 - Using Renewable Energy to Power Autonomous Underwater Vehicles
Sponsor:
Daniel MacDonald
Mehdi Raessi
Advisor:
David Rancour
Team Members:
Spencer Dowty (Team Leader)
Thomas Lattanzi
Antz-Lee Francois
Arthur Grizotte

## Slide 2
Operational View of MADWEC 3.0

## Slide 3: Charging Docking Station

## Slide 4
Purpose
MADWEC, the Maximal Asymmetric Drag Wave Energy Converter, is designed to be a small-scale local power platform for use in remote or deep-ocean locations.
Use renewable wave energy to charge autonomous underwater vehicles (AUV’s).
Allow for a decrease in manned missions to recover AUV’s when they are low on charge.
Reduce the cost and carbon footprint of AUV missions and surveying companies.
Develop a sustainable way of running underwater missions with small autonomous vehicles.

## Slide 5
1 | Design a charging station attached to the bottom of the MADWEC
2 | Autonomous underwater vehicle must dock at the station horizontally
3 | Charging should be compatible with a variety of different AUVs without requiring any alterations to the structure/hardware of the vehicle
4 | Should accommodate at least one AUV with the potential for expansion
5 | Determine a suitable battery to store the energy from the generators
6 | AC/DC converter to adapt the electrical output of the MADWEC
7 | Provide working winch to run “dry-testing” simulations in lab
8 | Accessible design and integration for MADWEC 4.0 team
Customer Requirements

## Slide 6
Engineering Requirements
Customer Rqmt No. | Engineering Rqmt No. | Engineering Requirement(s) Description | Justification and / or Comments | Test Method (IADT)
1 | 1.1 | Device installation to withstand being located around 55 meters below sea level | How the charging station is interfaced with the MADWEC per sponsor request | Testing
 | 1.2 | Charging station should not interfere with power generation of the MADWEC | Maximize power stored in battery as the docking mechanism creates more drag | Analysis
2 | 2.1 | AUVs must dock at a 90 degree angle to the MADWEC system | Accommodate for MADWEC’s orientation to allow for easy docking for the AUV | Demonstration/Testing
 | 2.1 | Mechanism should fall vertically, swinging at a -90 degree angle to minimize drag | This position would alleviate the additional drag forces introduced by the dock | Demonstration/Testing
3 | 3.1 | Device Compatibility - Universal charging to power 2-3 different types of AUVs | Remus 100, Riptide UUV 7, Oceanserver IVER3, and Bluefin 9 all recommended | Demonstration/Testing
 | 3.2 | Accommodate chosen AUVs of ~9 inch diameter without requiring any alterations | To avoid any installation constraints by requesting changes to existing AUVs | Inspection

## Slide 7
Customer Requirement No. | Engineering Requirement No. | Engineering Requirement(s) Description | Justification and / or Comments | Test Method (IADT)
4 | 4.1 | Charge at least one AUV while holding true to the average charge time of 6-8 hours | Guarantee full operation of MADWEC and allow AUV to run more missions. | Analysis/Testing
5 | 5.1 | Battery with 8kWh-10kWh capacity to store power from the six 50 W generators | More efficiently charge the AUVs while simultaneously not damaging the battery | Analysis/Testing
 | 5.2 | Provide a continuous 5-10 Amps to the AUV during the charge duration | Crucial to recharging the AUV lithium batteries properly to ensure safety | Testing
6 | 6.1 | Voltage regulator in order to step down/up and stabilize the AC signal from the generators rectifying it to 32 Volts DC | Need to regulate and stabilize voltage in order to charge the battery without any damage | Testing
7 | 7.1 | Develop program to oscillate in-lab winch with 1-2 meter amplitudes and 8-15 second periods for PTO testing | Allow for more accurate data collection for output of the generators’ technical potential | Demonstration/Testing
8 | 8.1 | Utilize obtainable software and hardware that will remain accessible for at least the next 3 years (MADWEC 4.0) | Should not be obsolete within the near future since MADWEC is a long term project | Demonstration
Engineering Requirements

## Slide 8
System Diagram

## Slide 9
Estimated Resources
Software:
EAGLE/KiCAD - Schematic and PCB Editing
Microsoft Visual Studios - Processor Programming
MATLAB - Oscillating Winch and Analyzing Data Files
All software is already paid for by the University.
Hardware:
Components for Voltage Rectifier
Battery Bank
Step Motor/Actuator
Charging cord for AUV
Transponder

## Slide 10
Constraints
Budget: SMAST East has a stringent account that allocates the money to both the MADWEC MNE and ECE teams of around 5,000 dollars
Collaboration: Working in parallel with the Mechanical Engineers responsible for Objective 1 who have a different schedule
Time: Strict deadlines for the project conflicting with SMAST process
Limited lab space at SMAST East and UMass due to construction
Limited information on generator output due to inconsistent wave patterns from the in-lab winch and data from the previous year
Limited alterations to the current MADWEC design from the rope to the one way clutch already being established as the final product

## Slide 11
GANTT Chart -September Task List

## Slide 12
GANTT Chart - October Task List

## Slide 13
GANTT Chart - November Task List

## Slide 14
Applicable Standards
IP Code - Waterproofing (IP67)
Institute of Printed Circuits Standards - PCB Design (IPC-2221)
Lithium Batteries - Battery Safety (IEC 62133-2:2017)
Storage of Batteries - Battery Safety (OSHA 1926.441)
RES - Renewable Energy Standard (CMR 14 + 15)
Cord Sets and Power Supply - (UL 817:Ed 11)
Electrical Testing - (BS EN 61010)
IEEE Code of Conduct & Ethics (IEEE 2, 5, 10)

## Slide 15
Ethical Issues
Source of Underwater Noise
Potential Threat to Marine Animals
Accidents in the Ocean
Extreme Overcrowding
Environmental Pollution
Job Reallocation

## Slide 16
References
“Applying IPC Standards to PCB Layout Design.” Cadence: PCB Design and Analysis, https://resources.pcb.cadence.com/blog/2021-applying-ipc-standards-to-pcb-layout-design
“Department of Transportation: Transportation of Lithium Batteries.” AUVAC, Department of Transportation, https://auvac.org/files/fdsys/pkg/fr-2014-08-06/pdf/2014-18146.pdf.
“Gantt Chart Template for Excel.” Vertex42, https://www.vertex42.com/ExcelTemplates/excel-gantt-chart.html.
“IP Rating Chart.” DSM&T Harsh Environment Connectors and Wire Harnessing, https://www.dsmt.com/resources/ip-rating-chart/
“Lithium-Ion Battery Standards.” USAID, International Electrotechnical Commission, https://www.usaid.gov/energy/powering-health/technical-standards/lithium-ion-batteries
“Massachusetts Renewable Energy Requirement.” Colonial power Group, https://colonialpowergroup.com/massachusetts-renewable-energy-requirement/
“REMUS 100h - Hydrographic Variant.” HII Technical Solutions, 23 Mar. 2021, https://tsd.huntingtoningalls.com/capabilities/unmanned-systems/unmanned-underwater-vehicles/remus100variants/remus100h/.
“Standards for Electrical Test Instruments and Test Leads.” Electrical Safety, https://elecsafety.com/standards-for-electrical-test-instruments-and-test-leads/
“System Diagram.” Lucid Chart: Intelligent Diagramming, https://www.lucidchart.com/pages/
“The Mysteries of IP65, IP66, and IP67 Rated Enclosures Explained.” Bud Industries, https://www.budind.com/blog/2014/02/the-mysteries-of-ip65-ip66-and-ip67-rated-enclosures-explained/
“1926.441 - Batteries and battery charging.” Occupational Safety and Health Administration,
https://www.osha.gov/laws-regs/regulations/standardnumber/1926/1926.441